Industrial portable air conditioner

User’s manual

Model: API24

IMPORTANT INFORMATION

Carefully read this instruction manual before you install or use your portable air conditioner. Please retain this manual for product warranty and for future reference.

CAUTION

- Make sure the inlet and outlet vents are never blocked.

- Ensure the appliance is on a stable, even surface when operating to avoid water leakage.

- Do not operate this unit in an explosive or corrosive atmosphere.

- When switched to cooling, only operate this unit in ambient temperatures between 17°C and 43°C.

- Clean the air filter frequently to ensure efficient operation.

- To prevent compressor damage when the unit has been operating and is turned off, please wait at least 3 minutes before restarting.

- This unit needs to be plugged into a 220V ~ 60Hz AC, 13 Amp power outlet.

- Do not use any extension cords with this unit.

- This unit is for indoor operation only.

- Open the adjustable air vent and extend the exhaust pipe (and drain pipe, if fitted) to the closest window before using.

- Only ever have a professional technician, manufacturer or service agent replace a damaged power cord.

- The batteries from the remote control must be removed and disposed of safely, before the appliance is scrapped.

- This appliance is not intended for use by persons (including children) with reduced physical, sensory or mental capabilities, or lack of experience and knowledge, unless they have been given supervision or instruction concerning use of the appliance by a person responsible for their safety.

- Children should be supervised to ensure that they do not play with the appliance.

- Keep this appliance at a distance of more than 40 cm from the wall or other obstacles.

- Unplug the unit before clean the appliance.

Important

To keep the cooling efficiency, please place the appliace according to following steps:

- Extend the exhaust pipe and keep its length less than 1000mm, do not fold the hose.

- Keep the side filter of this appliance at a distance of more than 500 mm from the wall or other obstacles.

- When the unit is stop to defrosting, the display will show “DF”.

CONGRATULATIONS ON YOUR

SELECTION OF A QUALITY

PORTABLE AIR CONDITIONER

This Air Conditioner has been designed and manufactured to the highest standards of modern engineering.

Our product not only provides you a remote control to help user operate all the functions easily and conveniently but also has below benefits:

- Moves easily from room to room on easy glide castors

- No installation required-just plug into any household

power outlet

- Powerful refrigerated air system cools down the ambience instantly whenever you want.

- Dehumidified and filtered air cycle improve breathing environments effectively.

- easy operate control panel provides easy-identifying manual operation.

- 24 hour programmable timer that can be used with either the air conditioning or dehumidification setting

- 220 Volt 60Hz operation

UNPACKING INSTRUCTIONS

1. Please put the product on flat ground before unpacking.

2. Unpack the carton, packing foam and supporting foam.

3. Disassembly the 4pcs bolts as showing A. use proper wrench to loosen the bolts.

4.  Take off the 2 pcs bracket as showing B.

5. Move the unit to the ground (better 2 persons work together and pay attention to the castors.

CONTENTS

1.  Grey color exhaust hose (long) x2

2.  Grey color exhaust hose (short) x2

3.  Round hose connector x 4

Parts name

- Control panel

- Air outlet

- castors

- front panel

- evaporator filter

- Back panel

- Condenser filter

- Upper drain hole

- Lower drain hole

- Hot air inlet

- Hot air outlet

- Cool air inlet

- Cool air outlet

CONTROL PANEL AND FUNCTION INTRODUCTION

- POWER KEY

Press to turn unit "ON" or "OFF".

- FUNCTION

Press this key to select cooling, dehumidifying.

- TEMPERATURE REGULATION KEY (UP)

Cooling mode (+): add 1℃ by pressing the button once until 30℃ at highest

- TEMPERATURE REGULATION KEY (DOWN)

Cooling mode (-): reduce 1℃ by pressing the button once until 17℃ at lowest

5.  L.E.D. DISPLAY

The display indicates the current setting temperature or the timer setting. When setting temperature or timer, the new setting is shown then the display returns the current set temperature.

- ※  The display is also used to show error codes when a fault occur, see “ERROR CODES”.

6.  SPEED

Press to select either LOW, MEDIUM, HIGH or AUTO fan speed.

If "AUTO" is selected (During cooling function),”HIGH” or "MEDIUM" or “LOW" will be selected automatically according to the difference between setting temperature and ambient temperature.

- PROGRAMMABLE TIMER

Programmable timer ON/OFF key.

TIMER-ON: The timer-on is used to turn on the unit automatically after the set time is over.

1. Press the "TIMER" key at stand-by status to set the time you desired.

2. Once the set hour has come to an end, the unit will turn on automatically.

3. Press the "POWER" key before time out, the setting time will be canceled and the unit will turn on.

4. You can set the function and fan speed while setting the timer.

TIMER-OFF: The timer-off is used to turn off the unit automatically after the setting time is over.

1. Press the "TIMER" key at operating status to set the time you desired.

2. Once the set hour has come to an end, the unit will turn off automatically.

3. Press the "POWER" key before the time out, the setting time will be canceled and the unit will turn off.

SLEEP CONTROL FUNCTION

1. While in cooling mode, press the SLEEP key to set the temperature. It increases1 ℃ after an hour and at most increases 2 ℃ after 2 hours.

2. Press the SLEEP key again can cancel the setting.

Note

When the water tank is full,"E4" will be displayed on the display panel. To resume operation, please remove the rubber cap of the drain hose to drain out the water firstly. The E4 warning will disappear after draining, and then you can restart the unit by pressing the POWER key.

IMPORTANT NOTICE

The product can evaporate condensate water and drain the water through exhaust hose automatically.

1. When the product is cooling, there is no need to install the drain pipe. Please make sure the drain hole is installed with rubber cap

2. When the product is dehumidifying, pull the rubber cap “①②”from the drain hole and install a suitable drain pipe

·Please remove the rubber cap to enhance the dehumidification ability.

When the water tank is full,"E4" will be displayed on the display panel. Please remove the rubber cap“①” of the drain hole to drain out the water first. After the "E4" disappeared, please restart the unit and then the unit can operate normally.

MAINTENANCE

Please cut off the power before cleaning.

FILTER CLEAN

Before clean the filter, please disassembly the front and back panel first then pull the filter edge and it can be put off.

Heat exchanger (CONDENSER/EVAPORATOR) clean

Use a brush attachment with a vacuum cleaner.

Shell clean

Clean the shell with wet cloth and wax it with soft cloth.

Please pull the filter up slightly according to the direction as shown in the figure to remove the filter screen for cleaning:

POWER SUPPLY

(1) Confirm the correct power.

(2) Insert the plug into the outlet firmly In order to prevent any dangerous leakage.

(3) Don’t pull power wire by force because it will cause damage to power wire.

PLACE FOR USE

- Because the machine distributes hot air, please don’t place or operate in a narrow place.

- In case of dangerous leak, don’t work the machine in a humid place.

- Don’t place the machine in a sunlit corner otherwise the unit might shut down due to the overheat and the color of the machine may soon fade out.

HELPFUL HINTS

The unit is fitted with a special thermal cut off device.
Please ensure the unit is not placed against objects which will obstruct air intake e.g. furniture or curtains as this will affect it's performance dramatically.

EXHAUST HOSE INSTALLATION

- Install the exhaust tube by rotating it clockwise onto the rear air outlet(picture ②) . Please ensure it is fully inserted before use.

Rotate the exhaust pipe anticlockwise (picture ①), and the exhaust the pipe can be put off.

TROUBLE SHOOTING

| Problem | Cause | Trouble shooting |
| --- | --- | --- |
| E1 | Electrical short on both temperature sensor and PCB | Contact maintenance station to repair |
| E2 | Electrical short of temperature sensor copper tube and PCB wiring | Contact maintenance station to repair |
| E4 | Indicates water tank full or possibly the incorrect wiring of plug | User needs to pull out the rubber stopper which is located at the bottom of the unit, to drain the water away. |

Specification

| model | PC70-IMB |
| --- | --- |
| Power source | 220V~60Hz |
| Power input(cooling) | 2800W |
| Cooling capacity | 7000W |
| Dehumidifying(30℃，80%RH) | 60liters/day |
| Refrigerant | R410A |
| Production dimensions(mm) | 518Wx540Dx972H |

(CE) N 842/2006:
R410A is a kind of fluorinated greenhouse gases covered by
the Kyoto Protocol.
Its total global warming potential (GWP) is 2088.

- Do not dispose of electrical appliances as unsorted municipal waste. Use separate collection facilities.

- Contact your local government for information regarding the collection systems available.

- If electrical appliances are disposed of in landfills or dumps, hazardous substances can leak into the ground water, polluting the food chain and     damaging health and well-being.